## Slide 1: Can technology prevent distracted driving crashes? Effectiveness of crash avoidance tech
Drive Smart Virginia
2017 Distracted Driving Summit
September 28, 2017
Jessica Cicchino

## Slide 2: Theoretical crash reductions if 100% effective
Crashes relevant to 4 crash avoidance systems
(FARS and GES, 2004-08)
 | all | injury | fatal
front crash prevention | 1,165,000 | 66,000 | 879
lane departure prevention | 179,000 | 37,000 | 7,529
side view assist | 395,000 | 20,000 | 393
adaptive headlights | 142,000 | 29,000 | 2,484
total unique crashes | 1,866,000 | 149,000 | 10,238

## Slide 4: Percent of crashes relevant to system where distraction was critical reason, National Motor Vehicle Crash Causation Survey
Kusano & Gabler, 2014
Chart: 
| front crash prevention | lane departure warning/prevention
crashes of all severities | 53 | 24

## Slide 5: Front crash prevention effectiveness

## Slide 6: Effects of forward collision warning and with autobrake on police-reported rear-end striking crashes
2010-15 data on police-reported rear-end striking crashes from 22 states with VINs
Merged police-reported data with insurance claim exposure data and data from automakers on collision avoidance features
Compared crash rates per insured vehicle year for vehicles with systems and same make/model/year vehicles without optional systems
Controlled for other collision avoidance technologies, calendar year, vehicle series/model year, state, vehicle density, rated driver age group, gender, marital status, deductible, insurance risk

## Slide 7: Study states
WY
WV
WI
WA
VT
VA
UT
TX
TN
SD
SC
RI
PA
OR
OK
OH
NY
NV
NM
NJ
NH
NE
ND
NC
MT
MS
MO
MN
MI
ME
MD
MA
LA
KY
KS
IN
IL
ID
IA
HI
GA
FL
DE
DC
CT
CO
CA
AZ
AR
AL
AK
Notes: In 2015, these 25 states made up 50% of the population, 53% of the VMT, and 55% of the deaths

## Slide 8: Effects of front crash prevention systems on rear-end strikes
Percent difference in crash rates
Chart: 
| City Safety | FCA (w/BSM +RCP) | Honda Accord camera (w/LDW) | Honda Accord radar (w/LDW +ACC) | Mercedes- Benz | Volvo | warning only pooled | Acura | Mercedes- Benz | Subaru (w/LDW) | Volvo (w/LDW) | autobrake pooled
crash | -0.43 | -0.2951 | -0.2168 | -0.2804 | -0.2453 | -0.3774 | -0.26575 | -0.4936 | -0.4401 | -0.5718 | -0.3855 | -0.49765
warning only
warning with autobrake
low speed
Notes: In 2-vehicle crash: impact to front of subject vehicle, rear of struck vehicle, and manner of collision is front-to-rear (first impact to struck vehicle not taken into account)
In 3+ vehicle crash: impact to front of subject vehicle, and manner of collision is front-to-rear

## Slide 9: Effects of front crash prevention systems on rear-end strikes with third-party injuries
Percent difference in crash rates
Chart: 
| City Safety | FCA (w/BSM +RCP) | Honda Accord camera (w/LDW) | Honda Accord radar (w/LDW +ACC) | Mercedes- Benz | Volvo | warning only pooled | Acura | Mercedes- Benz | Subaru (w/LDW) | Volvo (w/LDW) | autobrake pooled
crash | -0.44 | -0.3461 | -0.023 | 0.2206 | 0.047 | -0.367 | -0.179 | -0.688 | -0.561 | -0.826 | 0.103 | -0.59
warning only
warning with autobrake
low speed
Notes: Rear end strikes examined in 22 states
In 2-vehicle crash: impact to front of subject vehicle, rear of struck vehicle, and manner of collision is front-to-rear (first impact to struck vehicle not taken into account)
In 3+ vehicle crash: impact to front of subject vehicle, and manner of collision is front-to-rear

## Slide 11: Front crash prevention: Turned on?

## Slide 12: Percent of vehicle owners who reported driving with forward collision warning turned on
Chart: 
| Toyota | Volvo | Dodge and Jeep
always | 88 | 89 | 84
sometimes | 3 | 3 | 11
never | 0 | 2 | 0.5
unknown | 9 | 6 | 5
Notes: In surveys of drivers with various crash avoidance technologies, it’s apparent that lane departure warning is viewed as less desirable than other systems including forward collision warning.
However, these are self-report data

## Slide 13: On-off status of front crash prevention systems
By manufacturer
 | percent with system on | number observed
Chevrolet | 87 | 142
Cadillac | 92 | 206
Volvo | 94 | 52
Mazda | 95 | 20
Honda | 98 | 239
total | 93 | 659
Notes: 336 cases excluded. Ford system is always on (n=115); 122 Lexuses (PCS-off status (n=18) undetermined or default to on (n=104)); 70 Volvo XC90 (no FCP data); 1 Cadillac, 5 Chevrolet (FCA setting was selected as ‘other’); 6 Mazda (no SBS/SCBS in menu); 17 Toyota

## Slide 14: Front crash prevention testing and rating

## Slide 15: Front crash prevention ratings
vehicles without forward collision warning or autobrake; or vehicles equipped with a system that doesn’t meet NHTSA or IIHS criteria
vehicles earning 1 point for forward collision warning or 1 point in either 12 or 25 mph test
vehicles with autobrake that achieve 2-4 points for forward collision warning and/or performance in autobraking tests
vehicles with autobrake that achieve 5-6 points for forward collision warning and/or performance in autobraking tests

## Slide 17: Front crash prevention ratings
2013-17 models, as of September 2017
Chart: 
| Not qualified/not available | Basic | Advanced | Superior
2013 | 142 | 40 | 11 | 10
2014 | 116 | 53 | 28 | 19
2015 | 85 | 62 | 44 | 34
2016 | 58 | 59 | 48 | 63
2017 | 41 | 62 | 41 | 92

## Slide 18: Lane departure warning effectiveness

## Slide 19: Effects of lane departure warning on police-reported crashes
2009-15 data on police-reported crashes from 25 states with VINs
Crash types
  Single-vehicle, head-on and sideswipe crashes
  No vehicle turning, changing lanes, passing, merging or backing prior to crash
  Limited to roads with speed limits ≥ 40 mph, no snow/ice

## Slide 20: Effects of lane departure warning on relevant crash types of all severities
Chart: 
| GM (with FCW or AEB) | Honda Accord (with FCW) | Mazda | Mercedes-Benz (with FCW + AEB) | Subaru (with FCW + AEB) | Volvo (with FCW + AEB) | lane departure warning pooled
crashes | -0.134 | -0.1243 | -0.0584 | -0.3471 | -0.0155 | -0.101 | -0.11163
Percent difference in crash rates

## Slide 21: Effects of lane departure warning on relevant crash types with injuries
Chart: 
| GM (with FCW or AEB) | Honda Accord (with FCW) | Mazda (not enough data) | Mercedes-Benz (with FCW + AEB) | Subaru (with FCW + AEB) | Volvo (with FCW + AEB) | lane departure warning pooled
crashes | -0.2087 | -0.1916 | -0.6054 | -0.231 | -0.2072 | -0.21403
Percent difference in crash rates

## Slide 22: Observed and expected crashes for vehicles with lane departure warning
Not controlling for driver demographics
 | observed crashes | expected crashes | difference
all relevant crashes | 1189 | 1450.0 | -18%*
relevant crashes with injuries | 206 | 272.4 | -24%*
relevant fatal crashes | 2 | 13.9 | -86%*
*=statistically significant

## Slide 23: Lane maintenance systems: Turned on?

## Slide 24: Percent of vehicle owners who reported driving with lane-maintenance systems turned on
Chart: 
| Volvo lane departure warning | Infiniti lane departure warning | Infiniti lane departure prevention | Toyota lane departure prevention
always | 59 | 68.8 | 15.2 | 13
sometimes | 26 | 23.9 | 41.3 | 75
never | 14 | 7 | 21.7 | 12
unknown | 1 | 3 | 21.7 | 0
Notes: In surveys of drivers with various crash avoidance technologies, it’s apparent that lane departure warning is viewed as less desirable than other systems including forward collision warning.
However, these are self-report data

## Slide 25: Low use is likely limiting system effectiveness
2016 IIHS observations at dealership service centers
 | percent with system on | number observed
Ford/Lincoln | 21 | 115
Honda | 36 | 239
Chevrolet | 50 | 147
Cadillac | 56 | 204
Lexus/Toyota | 68 | 147
Volvo | 75 | 105
Mazda | 77 | 26
total | 51 | 983
Notes: Low use is likely limiting the effectiveness of the systems
Current study evaluated performance of Ford and GM as the use of vehicles with lane departure prevention systems was stark. (Note the table above includes use rates for lane departure warning and lane departure prevention)
  14 percent of Fords in lane departure prevention mode turned on
  64 percent of GMs with lane departure prevention turned on
Does system performance contribute to the low rate observed in Fords?

## Slide 26: GM lane departure warning on-off status by warning modality
 |  | percent with system on | number observed
beep | Cadillac | 33 | 18
 | Chevrolet | 39 | 66
 | total | 38 | 84
vibrating seat | Cadillac | 58 | 142
 | Chevrolet | 49 | 49
 | total | 56 | 191
Notes: NHTSA naturalistic study about 2000 vehicles 1/3 Equinox (beep only), 1/3 XTS, 1/3 SRX. 55% of sample aged 60-79.
setting Overall beeps safety seat safety seat with HUD
On 49.6 31.9 63.8 56.8
Off 50.4 68.1 36.3 43.2

## Slide 27: On-off status by maximum observable lane-maintenance intervention level
Percent with system on
Chart: 
| lane departure warning (n=547) | lane departure prevention (n=358) | active lane keeping (n=78)
crashes of all severities | 45.52 | 55.31 | 65.38

## Slide 29: Experiences with front crash prevention and lane departure prevention

## Slide 30: What system attributes influence the driver’s willingness to use vehicle technologies?
51 IIHS employees used one or more vehicles between August 2016 and July 2017
Nearly 50,000 miles and 2 years of driving
Vehicles used 104 times for 1 to 22 days and 6 days on average
Drivers completed surveys each day and after use
2016 Toyota Prius
2016 Infiniti QX60
2017 Audi Q7
2017 Audi A4
2016 Honda Civic
Notes: Not all vehicle technologies are well trusted and for different reasons

## Slide 31: I would keep this technology on all the time
Chart: 
| front crash prevention | lane departure prevention
Agreed/Strongly agreed | 79 | 54
Percentage of drivers who experienced a warning and agreed or strongly agreed

## Slide 32: I would keep this technology on all the time
Chart: 
| 2016 Toyota Prius | 2016 Honda Civic | 2016 Infiniti QX60 | 2017 Audi A4 | 2017 Audi Q7 | 2017 Audi A4 | 2016 Honda Civic | 2017 Audi Q7 | 2016 Toyota Prius | 2016 Infiniti QX60
Agreed/Strongly agreed | 57 | 67 | 82 | 88 | 91 | 91 | 80 | 38 | 36 | 35
Percentage of drivers who experienced a warning and agreed or strongly agreed
front crash prevention
lane departure prevention
Notes: The front crash prevention and lane departure prevention systems in these vehicles all provided a warning prior to automatic braking or steering correction by the vehicle.

## Slide 33: Which attributes of front crash prevention predicted the desire to keep the system on?
Drivers reported their level of agreement about front crash prevention:
  Always understood why a warning was issued or automatic braking occurred
  Warnings were useful
  Warnings felt urgent
  Warnings were not annoying
  Warnings occurred infrequently

## Slide 34: Always understood front crash warnings and automatic braking
Chart: 
| 2016 Honda Civic | 2016 Infiniti QX60 | 2017 Audi A4 | 2016 Toyota Prius | 2017 Audi Q7
Agreed/Strongly agreed | 42 | 64 | 69 | 71 | 82
Percentage of drivers who experienced a warning and agreed or strongly agreed

## Slide 35: Front crash warnings occurred infrequently
Chart: 
| 2016 Honda Civic | 2016 Infiniti QX60 | 2017 Audi A4 | 2016 Toyota Prius | 2017 Audi Q7
Agreed/Strongly agreed | 50 | 82 | 87 | 100 | 100
Percentage of drivers who experienced a warning and agreed or strongly agreed

## Slide 36: Which attributes of lane departure prevention were related to the desire to keep the system on?
Drivers reported their level of agreement with statements about lane departure prevention:
  Consistently detected lane markings on the roadway
  Warned only for unintentional lane departures
  Always understood why the warnings occurred
  Warnings felt urgent
  Warnings were not annoying
  Warnings were useful

## Slide 37: Lane departure prevention consistently detected lane markings
Chart: 
| 2017 Audi Q7 | 2016 Infiniti QX60 | 2016 Toyota Prius | 2016 Honda Civic | 2017 Audi A4
Agreed/Strongly agreed | 13 | 53 | 55 | 60 | 64
Percentage of drivers who experienced a warning and agreed or strongly agreed

## Slide 38: Lane departure warnings were not annoying
Chart: 
| 2016 Infiniti QX60 | 2016 Toyota Prius | 2017 Audi Q7 | 2016 Honda Civic | 2017 Audi A4
Agreed/Strongly agreed | 35 | 55 | 75 | 90 | 91
Percentage of drivers who experienced a warning and agreed or strongly agreed

## Slide 39: Lane departure warnings were useful
Chart: 
| 2016 Toyota Prius | 2017 Audi Q7 | 2016 Infiniti QX60 | 2016 Honda Civic | 2017 Audi A4
Agreed/Strongly agreed | 18 | 25 | 35 | 60 | 64
Percentage of drivers who experienced a warning and agreed or strongly agreed

## Slide 40: Summary
Front crash prevention and lane departure warning are preventing crashes, and many crashes they prevent are likely the result of distracted driving
Effectiveness of lane departure warning could be greater if drivers always kept it turned on
Modality, frequency, consistency, and type of warning or intervention can affect use

## Slide 41
Jessica B. Cicchino, Ph.D.
Vice President, Research
jcicchino@iihs.org